## Slide 1: Automatic SIMDization

## Slide 2: Vectorization and SIMDization
Vector supercomputers used for scientific computation
  Since CDC6600 and Cray-1
A lot of effort in vectorizing Fortran DO-loop
  Many scientific code do not have complex dependences in their innermost loops

## Slide 3: What is vectorization
a
b
c
d
e
f
g
h
i
j
k
l
m
n
o
p
OP(a)
OP(b)
OP(c)
OP(d)
Data in Memory:
VOP( a, b, c, d )
VR1
a
b
c
d
VR1
VR2
VR3
VR4
VR5
0
1
2
3
Vector Registers
Data elements packed into vectors
Vector length  Vectorization Factor (VF)
VF = 4
Vector operation
vectorization

## Slide 4: Vectorization
original serial loop: for(i=0; i<N; i++) { a[i] = a[i] + b[i]; }
loop in vector notation: for (i=0; i<N; i+=VF) { a[i:i+VF] = a[i:i+VF] + b[i:i+VF]; }
loop in vector notation: for (i=0; i<(N-N%VF); i+=VF) { a[i:i+VF] = a[i:i+VF] + b[i:i+VF]; } for ( ; i < N; i++) { a[i] = a[i] + b[i]; }
vectorization
Loop based vectorization
No dependences between iterations
vectorized loop
epilog loop
Vector section notation: a[i:j] is the vector composing of elements a[i], a[i+1], …, a[j]
Notes: - Simultanuously operate on different elements
- Prepare data in Small vectors (pack data elements)

## Slide 5: SIMD
SIMD (single instruction multiple data) architecture performs the same operation on multiple data elements in parallel

## Slide 6: Intel SSE
SSE (Streaming SIMD Extension) was introduced with Pentium III
Intel’s response to AMD’s 3DNow!
Floating point support
70 new instructions

## Slide 7: Intel SSE
Eight new 128-bit registers known as XMM0 through XMM7.
  With x86-64, 8 more added.
Each register packs together four 32-bit single-precision floating point numbers or two 64-bit double-precision floating point numbers or four 32-bit integers or eight 16-bit short integers or sixteen 8-bit bytes or characters.

## Slide 8: Intel SSE2
Introduced in the Pentium 4
Added new double precision floating point instructions
Allowed MMX instructions to operate on 128-bit XMM registers

## Slide 9: Intel SSE3
13 new instructions
Added instructions for digital signal processing
  Complex numbers
  Example:
    ADDSUBPS - (Add-Subtract-Packed-Single)
    Input: { A0, A1, A2, A3 }, { B0, B1, B2, B3 }
    Output: { A0 - B0, A1 + B1, A2 - B2, A3 + B3 }
Added instructions for hyperthreading support

## Slide 10: Intel SSSE3
Supplemental Streaming SIMD Extension 3 (SSSE3) introduced in the Core architecture
16 new instructions
Often confused with SSE4

## Slide 11: SSE4
Total of 54 new instructions added
SSE4.1 – introduced in Penryn
  47 new instructions
SSE4.2 – introduced in Core i7
  7 new instructions
SSE4a – supported by AMD
  4 instructions from SSE4 + 2 new instructions
Goes beyond multimedia applications

## Slide 12: AMD SSE5
Announced in August 2007
170 new instructions
Available 2011

## Slide 13: Intel AVX
Intel Advanced Vector Extensions
Suited for highly FP intensive workloads
Up to 256-bit wide vector FP data
3 and 4 operands supported
Power efficient, idle power usage is insignificant

## Slide 14: Intel AVX
> 200 legacy Intel SSE instructions are updated to handle flexible memory alignment and distinct source operands
< 100 legacy Intel SSE instructions are updated to support 256-bit vectors
< 100 new instructions
Broadcast, permute, fused multiply-add instructions.
4 operand instructions include: FMA, generalized shuffles, and blending of variables

## Slide 15: Intel AVX2 (2012)
expansion of most vector integer SSE and AVX instructions to 256 bits
three-operand general-purpose bit manipulation and multiply
three-operand fused multiply-accumulate support (FMA3)
Gather support, enabling vector elements to be loaded from non-contiguous memory locations
DWORD- and QWORD-granularity any-to-any permutes
vector shifts.

## Slide 16: Intel AVX-512 (2013)
Introduce EVEX prefix
Extensions to 512 bits
New registers
New instructions
  AVX-512 conflict detection (AVX-512CD) to help efficiently calculate conflict-free subsets of elements in loops that normally could not be safely vectorized.
Xeon Phi Knight’s Landing, Skylake-E

## Slide 17: An Important Alternative
AltiVec is a floating point and integer SIMD instruction set designed and owned by Apple, IBM and Freescale Semiconductor
  Implemented in the PowerPC and POWER
IBM updated it to VMX128 for the Xenon (Xbox 360)

## Slide 18: Vectorization vs. SIMDization
Difference is in the length of the vector
  SSE-type of SIMD, VL = 2 or 4
    Related to cache line size
  Vector supercomputers, VL = 128 or 256 or more
    Related to memory bandwidth
SSE-type generally has more instructions to permute data

## Slide 19: The most straightforward case
No loop dependences
Unit stride
Vectorization = Loop Distribution + Loop Unrolling

## Slide 20: Distribute and Unroll
for (i=0; i<N; i++) { d[i] = a[i] * b[i] + c[i]; e[i] = d[i] + e[j-1];
}
for (i=0; i<N; i++) { d[i] = a[i] * b[i] + c[i];
}
for (i=0; i<N; i++) { e[i] = d[i] + e[j-1];
}
for (i=0; i<N; i++) { temp[i] = a[i] * b[i];
d[i] = temp[i] + c[i];
}
for (i=0; i<N; i++) { e[i] = d[i] + e[j-1];
}
Original
Loop Distribution
Simplify ops

## Slide 21: Distribute and Unroll
for (i=0; i<N%4; i+=4) { temp[i] = a[i] * b[i];
d[i] = temp[i] + c[i]; temp[i+1] = a[i+1] * b[i+1];
d[i+1] = temp[i+1] + c[i+1];
temp[i+2] = a[i+2] * b[i+2];
d[i+2] = temp[i+2] + c[i+2]; temp[i+3] = a[i+3] * b[i+3];
d[i+3] = temp[i+3] + c[i+3];
}
for (; i<N; i++) { temp[i] = a[i] * b[i];
d[i] = temp[i] + c[i];
}
for (i=0; i<N; i++) { e[i] = d[i] + e[j-1];
}
Unroll
Group ops
Vectorize
for (i=0; i<N%4; i+=4) { temp[i] = a[i] * b[i];
temp[i+1] = a[i+1] * b[i+1];
temp[i+2] = a[i+2] * b[i+2];
temp[i+3] = a[i+3] * b[i+3];
d[i] = temp[i] + c[i];
d[i+1] = temp[i+1] + c[i+1];
d[i+2] = temp[i+2] + c[i+2]; d[i+3] = temp[i+3] + c[i+3];
}
for (; i<N; i++) { temp[i] = a[i] * b[i];
d[i] = temp[i] + c[i];
}
for (i=0; i<N; i++) { e[i] = d[i] + e[j-1];
}
for (i=0; i<N%4; i+=4) { temp[i:i+3] = a[i:i+3] * b[i:i+3];
d[i:i+3] = temp[i:i+3] + c[i:i+3];
}
for (; i<N; i++) { temp[i] = a[i] * b[i];
d[i] = temp[i] + c[i];
}
for (i=0; i<N; i++) { e[i] = d[i] + e[j-1];
}

## Slide 22: The complications
Mis-alignment
  Made worse by runtime alignment (i.e., alignment is not known at compile time, eg. 2-D array)
Non-unit stride
  Many apps do not have unit strides

## Slide 23
Peng Wu, Alexandre E. Eichenberger, and Amy Wang, “Efficient SIMD Code Generation for Runtime Alignment and Length Conversion”, Proceedings of the International Symposium on Code Generation and Optimization (CGO) 2005.
Views memory as streams of contiguous memory locations.

## Slide 24: vload / vstore
Vector loads and stores must occur at certain boundaries (related with the cache).
Example: assume 16-byte boundaries, and array a has a[0] starting at such a boundary. Then:
V1 = vload(a[2])
will load the elements a[0], a[1], a[2], and a[3] (i.e. the 16-byte block containing a[2]) into V1.

## Slide 25: SIMD Alignment Problem
Notes: Alignment matters in register too.
consider now the addition. First we load both b and c. You see that the b[1] and c[2] data are in the register at different offsets

## Slide 26: Three Policies
Zero-Shift Policy.
  Shifts each misaligned load stream to offset zero
  Shifts the store stream from offset zero to the alignment of the store address
Eager-Shift Policy.
  Shifts each load stream directly to the alignment of the store.
Lazy-Shift Policy.
  Pushes the shift towards the root of the expression tree as close as possible.
  Only for certain kinds of loops
The shifts are
virtual! Need to
implement them
using real
instructions!

## Slide 27: Loop-Level Simdization, Naïve Way
Notes: My goal is to walk through a simple example to illustrate what are the issues when programming for a SIMD unit like the VMC
single loop with 3 memory streams: A written into, B and C read
focusing on the first iteration, (grey boxes), ops to compute this simple add

## Slide 28: Solving the Alignment Problem
Data Reorganization Graph
  original graph with alignment label each load/store
  resolve alignment conflicts
offset 4
offset 12
vstore a[i+2]
offset 8
conflict:
reaching alignments
are not all identical
vload b[i+1]
vload c[i+3]
vadd

## Slide 29: Solving the Alignment Problem
set alignment
of streams
to zero
Data Reorganization Graph
  original graph with alignment label each load/store
  resolve alignment conflicts by adding “stream-shift” aligning operations
offset 4
offset 12
offset 8
stream-shift(4,0)
stream-shift(12,0)
stream-shift(0,8)
offset 0
vstore a[i+2]
vload b[i+1]
vload c[i+3]
vadd
To offset
From offet

## Slide 30: Loop-Level Simdization, Optimized Way
Notes: My goal is to walk through a simple example to illustrate what are the issues when programming for a SIMD unit like the VMC
single loop with 3 memory streams: A written into, B and C read
focusing on the first iteration, (grey boxes), ops to compute this simple add

## Slide 31: Optimized Solving of the Alignment Problem, Eager Policy
set to store alignment;
reduce stream-shift #
from 3 to 2
Data Reorganization Graph
  eagerly align to store alignment
offset 4
offset 12
offset 8
stream-shift(4,8)
stream-shift(12,8)
a[i+2:i+5] = V3
V1 = b[i+1:i+4]
V2 = c[i+3:i+6]
V3 = V1 + V2

## Slide 32: Optimized Solving of the Alignment Problem, Lazy Policy
lazily set to store align;
reduce stream-shift #
from 3 to 1
Data Reorganization Graph (slightly different “b[i+1] + c[i+1]” example)
  lazily align to store alignment
offset 4
offset 4
offset 8
stream-shift(4,8)
vstore a[i+2]
vload b[i+1]
vload c[i+1]
vadd

## Slide 33: The spoiler
The above requires knowledge about the alignment at compile time
To shift from x to y, must use
  Right shift if x ≤ y
  Left shift if x ≥ y
Zero shift policy can always be used
  Shifts are from x to 0, or 0 to y
  Less optimized

## Slide 34: A solution
Need a way to compute the shifts needed
Always use one (left) shift that can achieve the any shift amount
Insight: instead of looking at where the first element of the original array end up, look at what the first vector register element should come from

## Slide 35: vperm
vperm(v1, v2, k) selects bytes k, k + 1, …, k + V − 1 from a double-length vector constructed by concatenating v1 and v2, where V is the vector length
It is a “virtual” instruction that needs to be mapped to real SIMD processor instruction

## Slide 36: Implementing the shifts

## Slide 37: Left shift only

## Slide 38: Prepend
PrependW(S, x) denotes prepending x bytes to the beginning of a stream S of W-byte wide registers.
Note that, the W associated with prepend is a free variable that can be set to any value.
  It is used to convert lengths.
  If not used as such, W = V.
SkipW is the inverse of PrependW.

## Slide 39: Prepend

## Slide 40: Theorem

## Slide 41: An Example

## Slide 42: Another problem: Length conversion
In SIMD, it may be necessary to convert between data types of different lengths
Example, in other to add a byte with a 4-byte word, the former needs to be length converted to 4 bytes
  Note that the byte comes from a byte array

## Slide 43: VPACK and VUNPACK
VPACK(S, f) – packs a stream S by a factor f
VUNPACK(S, f) – unpacks a stream S by a factor f

## Slide 44: Offsets and lengths

## Slide 45: Relationship with Prepend

## Slide 46: Length conversion example
a is an array of short, b is an array of int. a[i+5] = (short)b[i+3]

## Slide 47: Another example
a is an array of int, c is an array of short. a[i+1] = (int)c[i+3]

## Slide 48: The IBM Cell SIMDizer Framework

## Slide 49: Loop Level Parallelism

## Slide 50: Basic Block Level Parallelism

## Slide 51: Entire Loop Parallelism

## Slide 52: Alignment!

## Slide 53: Size conversion

## Slide 54: Non-unit Stride

## Slide 55: Integrated Framework

## Slide 56: First Example

## Slide 57: First Example

## Slide 58: First Example

## Slide 59: First Example

## Slide 60: First Example

## Slide 61: Second Example

## Slide 62: Second Example

## Slide 63: Second Example

## Slide 64: Second Example

## Slide 65: End